## Slide 1
Sample Poster For reference only
Author1, Author2, Author 3, Author 4
1 The IET Chinaoffice
2 The Institution of Engineering and Technology
*youremailaddress@mail.com
Rotating components
Rotating Rectifier
Generator Control Unit
Pre-Exciter (PE)
Main Exciter (ME)
Main Generator (MG)
Load
D4 D5 D6
D1 D2 D3
Start Controller
a
b
c
A
B
C
1. Introduction
For the three-stage synchronous starter/generator (TSSG), the full-bridge uncontrolled rectifier is adopted instead of half- bridge uncontrolled reciter to improve the output current capability of the main exciter (ME). Generally, when using half-bridge rectifier, the pole numbers for the main generator (MG) and ME must not be equal or integral multiple of each other to reduce current shock to the excitation system when the MG’s armature winding is short-circuited. The constraint on pole ratio whether or not applies when using full-bridge rectifier is unknown.
Four MEs with different poles, as shown in Table 1, have
Poles of MG | Poles of ME | Pole ratio
6 | 2 | 3
6 | 4 | 1.5
6 | 6 | 1
6 | 12 | 0.5
Acknowledgment
This work was supported by National Natural Science Foundation of China (xxxx).
Fig. 1 Structure of the TSSG
been designed with the same outline dimension to analyze the excitation system’s transient performance.
In order to maximize validity of the analysis, the four MEs are designed to supply the MG with about 25A field current, at 8000rpm with 12A field current.
Tab. 1 Poles of the MG and the ME
2. Pole Ratio Influence
Currents of the MG’s Field Winding and Diodes：The increased armature winding current imposes strong demagnetizing effect on excitation magnetic field which results in a sharp increase of the field current of the MG, and the maximum rates of change are all around 269%. (Fig. 2)
As shown in Fig. 2(b), three or two diodes located in upper or lower legs share the field surge current, fully reducing current shock to the rectifier. Fig. 2(a) indicates that certain diode itself shares the surge current which is unwanted.
Armature current of the ME: When the maximum rate occurs, equivalently six diodes absorb the field surge current. Still, for the four-poles ME, only one diode current conducts the field surge current with which the phase armature winding connected conducts the surge current directly. In other word, the constraint on pole ratio is inapplicable.
Exciter | Rate of change of MG current (%) |  | Rate of change of ME current (%) | 
 | Armature | Field | Diode | Armature
2 poles | 145.7 | 269.8 | 74.6 | 44.9
4 poles | 146.6 | 270.8 | 270.8 | 270.8
6 poles | 144.1 | 267.8 | 108.2 | 74.2
12 poles | 145.5 | 269.3 | 132.3 | 130.0
Exciter |  | Diodes (%) | Armature (%)
4-poles | original | 270.8 | 270.8
 | redesigned | 100.8 | 72.1
12-poles | original | 132.3 | 130.0
 | redesigned | 89.2 | 51.8
Tab. 3 Maximum current rates of change for the excitation system
Tab. 2 Maximum rates of change for currents
3. Influence of Operation Mode of the Rectifier
When the rectifier operates at mode 2 or 3, shortly after the short-circuit of the MG, a constant short-circuit is imposed on the ME and there’s a long period for four diodes conducting, which can be called as operation mode 4.
For the rectifier working with the 4-poles ME, it operates at mode 1 and the surge current cannot change its operation mode, which brings the excitation system with severe current shock. The rectifiers of the other three excitation systems operate at mode 3, mode 3 and mode 2 respectively. (Fig. 3-4)
One assumption is set forth that the operation mode of rectifier matters much more than the pole ratio. To prove this assumption, the 4-poles ME and 12-poles ME have been redesigned to make the rectifiers operate at mode 3 (Fig. 6-7)
Simulation results show that it’s better to design the TSSG to make the rectifier work at mode 2 or 3.
4. Conclusion
For TSSG, when adopting the three-phase full-bridge rectifier, the constraint of pole ratio is no longer applicable.
In order to reduce the current shock to the excitation system when the MG’s armature winding is short-circuited, one should design the TSSG to make the rectifier operate at mode 2 or 3 on the basis of ensuring the excitation system’s output current capability.
Fig. 2 Diode currents and field current of the MG
(a) Four-poles ME
Fig. 3 Armature currents of the ME
(b) Twelve-poles ME
(b) Twelve-poles ME
(b) Twelve-poles ME
Fig . 6 Armature currents of the redesigned MEs
(b) Twelve-poles ME
Fig. 4 Terminal voltage of MG’s field winding with different MEs
0 4 296
300 304
445 450
0
50
100
150
200
Voltage (V)
Time (ms)
(a) Four-poles ME
0 4 300 302 304
445
450
0
50
100
Voltage (V)
Time (ms)
Fig. 5 Diode currents and field current of MG with redesigned MEs
0 4
445 450
0
20
40
60
80
100
Current (A)
300 304 308
Time (ms)
(a) Four-poles ME
Field current of MG
D4 D6 D2
D5 D1 D3
0
4 300 304
445
450
0
20
40
60
80
100
Current (A)
Time (ms)
Field current of MG
D4 D6 D2
D5
D1
D3
(a) Four-poles ME
0 4 300 304
445
450
0
20
40
60
80
100
120
C urrent (A )
Time (ms)
Field current of MG
D4 D6
D5 D1
D2
D3
0 4
445 450
0
20
40
60
80
100
Current (A)
300 304
Time (ms)
(a) Four-poles ME
Field current of MG
D4 D6 D2
D5 D1 D3
300
304 308
445 450
-80
0 4
-60
-40
-20
0
20
40
60
80
100
Current (A)
Time (ms)
Phase a
Phase b Phase c
445
450
-40
-30
-20
-10
0
10
20
30
40
Current (A)
-50
0 4 300 304
Time (ms)
(b) Twelve-poles ME
Phase a Phase b
Phase c
0 4
300
450
-40
-20
0
20
40
C urrent (A )
304 308 445
Time (ms)
Phase a Phase b Phase c
0 4 300 445 450
-40
-30
-20
-10
0
10
20
30
40
Current (A)
Time (ms)
Phase a
Phase b
Phase c
0
0 4 300 304 445 450
100
200
300
Voltage (V)
Time (ms)
0 4 300 304 448 450
0
50
100
150
200
250
300
V oltage (V)
Time (ms)
(a) Redesigned four-poles ME
(b) Redesigned twelve-poles ME Fig. 7 Terminal voltage of MG’s
field winding
Sample